## Slide 1: 7th International Conference on VVER Fuel Performance Modeling and Experimental Support Bulgaria Albena Congress Center 17-21 September 2007
EXPERIENCE OF
REPU FUEL FABRICATION AND OPERATION
IN VVER REACTORS
ОАО MASHINOSTROITELNY ZAVOD, Elektrostal, Russia
ОАО TVEL, Moscow, Russia
FGUP VNIINM, Moscow, Russia
RRC KURCHATOV INSTITUTE, Moscow, Russia
1

## Slide 2: INTRODUCTION
The continuous evolution and operation of power reactors assumes re-cycling or, in other words, return of plutonium and reprocessed uranium (RepU) to the front-end of the cycle. At present, Russia is among the countries that have industrial experience in utilization of the RepU fuel.
The necessity of reprocessing is urged by economic reasons, related to availability of natural uranium and residual content of U-235 in spent fuel. For instance, in the spent VVER-1000 fuel (up to 60 MW*d/kgU) the residual content of U-235 is higher than in natural uranium.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
2

## Slide 3: INTRODUCTION
RepU:
Usually U-238, U-235,
Extra U-236, U-234, U-232
Increased neutron absorption
Change of the radiation situation
U-236 content compensation
Limitation of the content of the even isotopes
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
3

## Slide 4: DEVELOPMENT PROGRAM
The development program included:
compensation factor calculation and recommendations;
nuclear design of the fuel reloads;
safety analysis;
the lead FAs operation licensing;
the lead FAs fabrication;
the lead FAs operation.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
4

## Slide 5
Compensation factor
Implementation of the RepU requires maintaining of the fuel cycle time and loading patterns at NPPs.
The variation in nominal U-235 enrichment is allowed by technical requirements for nuclear fuel. The now adopted absolute accuracy of the U-236 compensation technique can be compared to the maximum value of the permissible deviation, and must be considered for at calculating the mechanical aspect of margin factor, thus, increasing it.
Presently, when compensating U-236 with initial RepU enrichment of 4%, the factor of 0.3 is used.
The U-234 compensation makes about 10% of the re-enrichment value compensating the U-236 content which is appropriate in cases when the entire core is loaded with high content of U-234 RepU fuel – this, however, has no application in practice.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
5
DEVELOPMENT PROGRAM

## Slide 6: DEVELOPMENT PROGRAM
Nuclear design of the fuel reloads
RepU VVER-440 steady-state fuel cycle parameters
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
6
Parameter | Value
Reactor thermal power, MW | 1375
Number of FAs in the core | 313
Enrichment profiling in FA cross-section | Applicable
Time between reloads, months | 12
Loading pattern | L3P (Low Leakage Loading Pattern)
Number of loaded FAs | 66
Average enrichment of fuel reloaded, % | 3,91
Years of operation of discharged FAs - average - maximum | 4,74 5
Average burn-up of discharged fuel, MW*d/kgU | 43,9

## Slide 7: DEVELOPMENT PROGRAM
Nuclear design of the fuel reloads
RepU VVER-1000 steady-state fuel cycle parameters
Parameter | Value
Reactor thermal power, MW | 3000
Number of FAs in the core | 163
Enrichment profiling in FA cross-section | Applicable
Time between reloads, months | 12
Type of burnable absorber | Integrated Gd2O3
Loading pattern | Decreased Leakage
Number of loaded FAs | 48
Average enrichment of fuel reloaded, % | 4,38
Average burn-up of discharged fuel, MW*d/kgU | 48,5
7

## Slide 8: DEVELOPMENT PROGRAM
Safety analysis
Cases for justification of the RepU fuel nuclear safety:
FA criticality in water;
Transport package;
Fresh fuel racks;
Container for fresh FAs ;
Racks for fuel storage in spent fuel ponds;
Canister;
Cask for spent fuel transport.
The presence of U-236 reduces multiplicity factor in all the above cases. In the standard operation mode, allowing for possible technical elements deviations, the required subcriticality is still ensured.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
8

## Slide 9: DEVELOPMENT PROGRAM
The lead FAs operation licensing
Licensing of the trial operation required implementation of the following:
The TOB RU (Safety Analysis Report) Supplement on FAs operation justification;
Program and procedures for in-pile testing of the lead RepU FAs;
Acceptance tests of the lead FAs;
Revision of operating documents for the fuel loads of respective units.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
9

## Slide 10: DEVELOPMENT PROGRAM
Lead FAs fabrication
Actions:
Time limits for processing RepU into fuel assemblies;
Reduced number of manual operations
Tightened monitoring of radiation situation
All the normative requirements related to radiation safety were kept during the FAs fabrication.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
10

## Slide 11: DEVELOPMENT PROGRAM
Lead FAs fabrication
Isotopic composition of the RepU fuel pellets for VVER reactors
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
Isotope | Content, %
235U | 4,098 – 4,176
236U | 0, 3441 – 0,5407
234U | 0,0448 – 0,0490
232U | 0,77*10-7 – 1,35*10-7
11

## Slide 12: DEVELOPMENT PROGRAM
Trial FAs operation.
Experience of RepU Fuel Operation in VVER-440. Kola-2 reactor.
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
Description | Fuel campaign |  |  |  | 
 | 25 | 26 | 27 | 28 | 29
Quantity of FAs operated for 1 year, pcs | 12 | - | 62 | 48 | 66
Quantity of FAs operated for 2 years, pcs | - | 12 | - | 62 | 48
Quantity of FAs operated for 3 years, pcs | - | - | 10 | - | 62
Quantity of FAs operated for 4 years, pcs | - | - | - | 10 | -
Quantity of FAs operated for 5 years, pcs | - | - | - | - | 3
Total, pcs | 12 | 12 | 72 | 120 | 179
Maximum burn-up of discharged FAs, MW*d/kgU |  | 22,0 |  | 42,4 | 
12

## Slide 13: DEVELOPMENT PROGRAM
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
Trial FAs operation.
Experience of RepU Fuel Operation in VVER-1000. Kalinin-2 reactor.
Description | Fuel campaign |  |  |  | 
 | 15 | 16 | 17 | 18 | 19
Quantity of FAs operated for 1 year, pcs | 12 | - | 18 | 48 | 48
Quantity of FAs operated for 2 years, pcs | - | 12 | - | 18 | 48
Quantity of FAs operated for 3 years, pcs | - | - | 12 | - | 18
Quantity of FAs operated for 4 years, pcs | - | - | - | 3 | -
Quantity of FAs operated for 5 years, pcs | - | - | - | - | -
Total, pcs | 12 | 12 | 30 | 69 | 114
Maximum burn-up of discharged FAs, MW*d/kgU |  |  | 45,3 | 48,2 | 

## Slide 14: CONCLUSION
EXPERIENCE OF REPU FUEL FABRICATION AND OPERATION IN VVER REACTORS
The work that has been accomplished by the Russian institutions, made it possible to develop and introduce trial operation of the RepU fuel assemblies for both VVER-440 and VVER-1000 reactors.
Kola-2 was transferred into commercial operation with the RepU fuel.
The trial operation of the RepU TVSAs is continuing for Kalinin-2.
The justification results of nuclear design, of radiation and nuclear safety during fuel manufacturing and handling as well as operational experience of commercial lots show that the RepU fuel characteristics comply with the limitations adopted in the VVER reactor designs.
14